## Slide 1: CHAPTER 2 Data Manipulation
数 据 操 控

## Slide 2
讲课人比较菜，可能有大量讲错的
讲课人没有经验，不知道要干什么
PPT由课本上语句拼接而成
希望及时提出更好的看法

## Slide 3: 2.1 Computer Architecture

## Slide 4: 2.1 Computer Architecture
The circuitry in a computer that controls the manipulation of data is called the central processing unit, or CPU (often referred to as merely the processor).
the machine’s main circuit board (called the motherboard)
Mobile Internet Devices (MID)
microprocessors

## Slide 5: CPU Basics
A CPU consists of three parts：
  the arithmetic/logic unit
  the control unit
  the register unit
    general-purpose registers
    special-purpose registers
For the purpose of transferring bit patterns, a machine’s CPU and main memory are connected by a collection of wires called a bus.
Notes: Figure 2.1 CPU and main memory connected via a bus
Figure 2.2 Adding values stored in memory

## Slide 6: CPU Basics
Registers are used to hold the data immediately applicable to the operation at hand.
Main memory is used to hold data that will be needed in the near future.
Mass storage is used to hold data that will likely not be needed in the immediate future.
Cache memory is a portion (perhaps several hundred KB) of high-speed memory located within the CPU itself.
Spatial Locality, Temporal Locality
Notes: 缓存之所以有效，主要是因为程序运行时对内存的访问呈现局部性（Locality）特征。这种局部性既包括空间局部性（Spatial Locality），也包括时间局部性（Temporal Locality）。有效利用这种局部性，缓存可以达到极高的命中率。

## Slide 7: The Stored-Program Concept
Early computers were not known for their flexibility—the steps that each device executed were built into the control unit as a part of the machine. To gain more flexibility, some of the early electronic computers were designed so that the CPU could be conveniently rewired. This flexibility was accomplished by means of a pegboard arrangement similar to old telephone switchboards in which the ends of jumper wires were plugged into holes.

## Slide 8: The Stored-Program Concept
The idea of storing a computer’s program in its main memory is called the stored-program concept and has become the standard approach used today.

## Slide 9: 2.2 Machine Language

## Slide 10: 2.2 Machine Language
To apply the stored-program concept, CPUs are designed to recognize instructions encoded as bit patterns. This collection of instructions along with the encoding system is called the machine language. An instruction expressed in this language is called a machine-level instruction or, more commonly, a machine instruction.

## Slide 11: The Instruction Repertoire
reduced instruction set computer (RISC)
  Advanced RISC Machine (ARM)
  low power consumption
complex instruction set computer (CISC)
Regardless of the choice between RISC and CISC, a machine’s instructions can be categorized into three groupings:
  the data transfer group
  the arithmetic/logic group
  the control group.

## Slide 12: Data Transfer
A request to fill a general-purpose register with the contents of a memory cell is commonly referred to as a LOAD instruction; conversely, a request to transfer the contents of a register to a memory cell is called a STORE instruction.
I/O instructions
Notes: Since these instructions handle the input/output (I/O) activities of the machine, they are called I/O instructions and are sometimes considered as a category in their own right.
1. Why might the term move be considered an incorrect name for the operation of moving data from one location in a machine to another?

## Slide 13: Arithmetic/Logic
the basic arithmetic operations
the Boolean operations AND, OR, and XOR
allows the contents of registers to be moved to the right or the left within the register
  the bits that “fall off the end” of the register are merely discarded (SHIFT)
  used to fill the holes left at the other end (ROTATE).

## Slide 14: Control
This group contains many of the more interesting instructions in a machine’s repertoire, such as the family of JUMP (or BRANCH) instructions used to direct the CPU to execute an instruction other than the next one in the list.
These JUMP instructions appear in two varieties: unconditional jumps and conditional jumps.
Notes: Figure 2.3 Dividing values stored in memory

## Slide 15: Variable-Length Instructions
This consistency streamlines the task of fetching instructions and is characteristic of RISC machines.
CISC machines, however, have machine languages whose instructions vary in length.
Notes: To simplify explanations in the text, the machine language used for examples in this chapter (and described in Appendix C) uses a fixed size (two bytes) for all instructions. Thus, to fetch an instruction, the CPU always retrieves the contents of two consecutive memory cells and increments its program counter by two. This consistency streamlines the task of fetching instructions and is characteristic of RISC machines. CISC machines, however, have machine languages whose instructions vary in length. Today’s Intel processors, for example, have instructions that range from single-byte instructions to multiple-byte instructions whose length depends on the exact use of the instruction. CPUs with such machine languages determine the length of the incoming instruction by the instruction’s op-code. That is, the CPU first fetches the op-code of the instruction and then, based on the bit pattern received, knows how many more bytes to fetch from memory to obtain the rest of the instruction.

## Slide 16: An Illustrative Machine Language
The encoded version of a machine instruction consists of two parts: the op-code (short for operation code) field and the operand field.
Notes: Figure 2.5 The composition of an instruction for the machine in Appendix C
Figure 2.6 Decoding the instruction 35A7
Figure 2.7 An encoded version of the instructions in Figure 2.2

## Slide 17: Appendix C

## Slide 18: 2.3 Program Execution

## Slide 19: 2.3 Program Execution
Two of the special purpose registers within the CPU:
  the instruction register
  the program counter
The instruction register is used to hold the instruction being executed. The program counter contains the address of the next instruction to be executed, thereby serving as the machine’s way of keeping track of where it is in the program.

## Slide 20: 2.3 Program Execution
The CPU performs its job by continually repeating an algorithm that guides it through a three-step process known as the machine cycle.
Fetch
  Retrieve the next instruction from memory (as indicated by the program counter) and then increment the program counter.
Decode
  Decode the bit pattern in the instruction register.
Execute
  Perform the action required by the instruction in the instruction register.
Notes: Figure 2.8 The machine cycle
Figure 2.9 Decoding the instruction B258

## Slide 21: Comparing Computer Power
A computer’s clock is a circuit, called an oscillator, that generates pulses that are used to coordinate the machine’s activities—the faster this oscillating circuit generates pulses, the faster the machine performs its machine cycle.
Different CPU designs might perform different amounts of work in one clock cycle, and thus clock speed alone fails to be relevant in comparing machines with different CPUs.
If you are comparing a machine based on an Intel processor to one based on ARM, it would be more meaningful to compare performance by means of benchmarking, which is the process of comparing the performance of different machines when executing the same program, known as a benchmark.
Notes: Figure 2.8 The machine cycle
Figure 2.9 Decoding the instruction B258

## Slide 22: An Example of Program Execution
Notes: Figure 2.10 The program from Figure 2.7 stored in main memory ready for execution
Figure 2.11 Performing the fetch step of the machine cycle

## Slide 23: Programs Versus Data
The machine alone has no way of knowing what is data and what is program
In fact, providing programs and data with a common appearance in a machine’s memory has proved a useful attribute because it allows one program to manipulate other programs (or even itself) the same as it would data.

## Slide 24: 2.4 Arithmetic/Logic Instructions

## Slide 25: Logic Operations
These operations(AND, OR, and XOR) can be extended to bitwise operations that combine two strings of bits to produce a single output string by applying the basic operation to individual columns.
This use of the AND operation is an example of the process called masking. Here one operand, called a mask, determines which part of the other operand will affect the result.
bit map
Notes: 按位运算
屏蔽 掩码
位映射

## Slide 26: Rotation and Shift Operations
circular shift, also called a rotation
  place the bit that fell off the right end in the hole at the left end
logical shift
  discard the bit that falls off the edge and always fill the hole with a 0
arithmetic shifts
  shifts that leave the sign bit unchanged
Notes: Figure 2.12 Rotating the bit pattern 65 (hexadecimal) one bit to the right

## Slide 27: Arithmetic Operations
Some small CPUs are designed with only the add or perhaps only the add and subtract instructions.
floating-point values
Notes: First, we have already seen that subtraction can be simulated by means of addition and negation. Moreover, multiplication is merely repeated addition and division is repeated subtraction.

## Slide 28: THANK YOU